## Slide 1: Chapter 5
Image pre-processing
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 2: Image pre-processing
Pixel brightness transformations
Geometric transformations
Local pre-processing
  Image smoothing, edge detection, line detection, corner detection, and region detection.
Image restoration
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 3: Introduction to linear integral transforms
Image filtering (Chapter 3)
  An application of a linear integral transform in image processing
  Filtering can be performed in either spatial or frequency domains.
  There is one-to-one mapping between the spatial and frequency domains.
  For linear operations, these two ways should provide equivalent results.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 4: Local pre-processing in the frequency domain
Spatial frequency filtering
  Assume that is an input image and is its Fourier transform.
  A convolution filter can be represented by its Fourier transform .
  The Fourier transform of the filter output after an image has been convolved with the filter can be computed in the frequency domain
  where represents an element-by-element multiplication of matrices and (not matrix multiplication).
  The filtered image can be obtained by applying the inverse Fourier transform to (equation 3.28).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 5: Local pre-processing in the frequency domain
Some basic examples of spatial frequency filtering
  Linear low-pass frequency filters
  Linear high-pass frequency filters
  Linear band-pass frequency filters
  (http://www.ejectamenta.com/Imaging-Experiments/fourierimagefiltering.html)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 6: Local pre-processing in the frequency domain
Low-pass frequency-domain filtering
  Noise can be suppressed.
  A blurred image
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 7: Local pre-processing in the frequency domain
High-pass frequency-domain filtering
  Edge can be enhanced.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 8: Local pre-processing in the frequency domain
Bend-pass frequency-domain filtering
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 9: Local pre-processing in the frequency domain
Periodic noise removal
  (a) Noisy image
  (b) Image spectrum used for image reconstruction
    The areas of frequencies corresponding with periodic vertical lines are filtered out.
  (c) Filtered image
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 10: Local pre-processing in the frequency domain
Filters which prove useful for filtering in the frequency domain
  Gaussian filter
  Butterworth filter
Choose an isotropic (等向的) filter for simplicity
and let be a parameter of the filter called the cut-off frequency.
PS. An isotropic filter treats all axes equally.
A cutoff frequency is a boundary in a system's frequency response at which energy flowing through the system begins to be reduced rather than passing through.
  (截止頻率(Cutoff frequency)是指一個系統的輸出信號能量開始大幅下降的邊界頻率。)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 11: Local pre-processing in the frequency domain
The Gaussian low-pass filter
  The cut-off frequency coincides (一致) with the dispersion .
  The Fourier spectrum of a low-pass Gaussian filter is
The Butterworth low-pass filter
  The usually Butterworth filter degree is .
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 12: Local pre-processing in the frequency domain
High-pass filter
  The high-pass filter is created easily from the low-pass filter.
  If the Fourier frequency spectrum of a low-pass filter is , the high-pass filter can be created by just flipping it vertically
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://www.mathworks.com/matlabcentral/mlc-downloads/downloads/submissions/46812/versions/1/screenshot.jpg

## Slide 13: Local pre-processing in the frequency domain
Homomorphic (同態的) filtering
  Another useful pre-processing technique operating in the frequency domain
  Homomorphic filtering is used to remove multiplicative noise.
  PS: In signal processing, the term multiplicative noise (乘性雜訊) refers to an unwanted random signal that gets multiplied into some relevant signal during capture, transmission, or other processing. An important example is the speckle noise (斑點雜訊) commonly observed in radar imagery.
The assumption is the image function can be factorized as a product of two independent multiplicative components in each pixel.
where is the illumination and is the reflectance
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 14: Local pre-processing in the frequency domain
Homomorphic filtering
  Apply a logarithmic transform to the input image
  If the image is converted to Fourier space then its additive components remain additive due to the linearity of the Fourier transform.
  Assume that the Fourier spectrum is filtered by the filter and the spectrum is the result.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
We use a high-pass filter in the log domain to remove the low-frequency illumination component while preserving the high-frequency reflectance component.
http://blogs.mathworks.com/steve/2013/06/25/homomorphic-filtering-part-1/
Homomorphic filtering
https://zh.wikipedia.org/wiki/%E5%90%8C%E6%85%8B%E6%BF%BE%E6%B3%A2

## Slide 15: Homomorphic filtering
Having the filtered spectrum , we can return to spatial coordinates using the inverse Fourier transform.
The result image filtered by the homomorphic filter is given by
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 16: Homomorphic filtering
http://blog.csdn.net/bluecol/article/details/45788803
1. 一張影像可以表示為照度(illumination)分量和反射(reflectance)分量的乘積。 在時域上這兩者不可分離，但是經傅立葉轉換後在頻域中則可以線性分離。
2. 由於照度變化較小，可以視為影像低頻成份；而反射相對變化較大，可視為高頻成份。
https://zh.wikipedia.org/wiki/%E5%90%8C%E6%85%8B%E6%BF%BE%E6%B3%A2

## Slide 17: Line detection by local pre-processing operators
Line finding operators
  Line finding operators aim to find very thin curves in the image.
    It is assumed that curves do not bend sharply.
    Such curves and straight lines are called lines.
    We assumed that the width of the lines is approximately one or two pixels.
    For examples, some convolution kernels are
    Suggestion: Thresholded edges are usually wider than one pixel, and line thinning techniques may give a better result.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 18
Edge Reinforcement with Thinning
(a) (c) (e) (g)
(b) (d) (f) (h)

## Slide 19: Detection of corners
Corners
  One kind of interest points for the correspondence problem.
  Corners in images can be located using local detector.
  Interest points are obtained by thresholding the result of the corner detector.
  Corners serves better than lines when the correspondence problem is to be solved.
  Why?
  The aperture problem. (孔徑問題)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 20: Detection of corners
Corners
  Edge detectors themselves are not stable at corner.
  This is natural as the gradient at the tip of the corner is ambiguous.
  Figure 5.32 shows a sharp corner.
  Near the corner there is a discontinuity in the gradient direction, and this observation is used in corner detectors.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 21: Detection of corners
Corners
  A corner in an image can be defined as a pixel in whose immediate neighborhood there are two dominant(明顯的), different edge directions.
  Corner detectors are not usually very robust. One can detect corners using two or more images.
  Corner detector
    Moravce detector
    Zuniga-Haralick operator
    Harris corner detector
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 22: Detection of corners
Moravce corner detector
  Moravce detector is maximal in pixels with high contrast, which are corners and sharp edges.
  The Moravec operator MO is given by
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 23: Detection of corners
Zuniga-Haralick operators
  Zuniga-Haralick operators are based on the facet model.
  The image function is approximated in the neighborhood of the pixel by a cubic polynomial with coefficients .
  The Zuniga-Haralick operators ZH is given by
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 24: Detection of corners
Harris corner detector
  Harris corner detector improved upon Moravec’s by considering the differential of the corner score (sum of square difference).
  Consider a 2D gray-scale image
    An image patch is taken and is shifted by .
    The sum of square differences between values of the image given by the patch and its shifted variant by is given by
    A corner must have a high response of for all .
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
http://blog.csdn.net/jwh_bupt/article/details/7628665

## Slide 25: Detection of corners
Harris corner detector
  If the shifted image patch is approximated by the first-order Taylor expansion
  Then the minimum of can be obtained analytically.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 26: Detection of corners
Harris corner detector
  Since that
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 27: Detection of corners
Harris corner detector
The Harris matrix represents one half the second derivative of the image patch around the point
is
The Harris matrix is symmetric and positive semi-definite.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://en.wikipedia.org/wiki/Positive-definite_matrix

## Slide 28: Detection of corners
Harris corner detector
Let be the eigenvalues of three distinct cases can occur:
  Both eigenvalues are small.
    Image is flat at the examined pixel.
    There is no edges or corners in this location.
  One eigenvalue is small and the second large.
    The local neighborhood is ridge(山脊)-shaped.
    Significant change of occurs if a small movement is made perpendicularly to the ridge.
  Both eigenvalues are rather large.
    A small shift in any direction causes significant change of .
    A corner has been found.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 29: Eigenvalue and Eigenvector
Given a square matrix A, the eigenvalue can be obtained by
For example
  The matrix defines a linear transformation of the real plane.
  The eigenvalues of matrix A are given by
  The roots of this equation are λ = 1 and λ = 3.
  Considering first the eigenvalue λ = 3, we have
  After matrix-multiplication
    This matrix equation represents a system of two linear equations
  2x + y = 3x and x + 2y = 3y.
    Both the equations reduce to the single linear equation x = y.
    To find an eigenvector, we are free to choose any value for x,
    so by picking x=1 and setting y=x, we find the eigenvector to be

## Slide 30: Detection of corners
Harris corner detector
Harris suggested that exact eigenvalue computation can be avoided by calculating the response function.
(1) If then and .
(2) Moreover, is a parameter, values from 0.04 to 0.15.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 31: Detection of corners
Examples of Harris corner detector
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 32: Harris corner detector
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
Algorithm 5.5 Harris corner detector
1. Filter the image with a Gaussian.
2. Estimate intensity gradient in two perpendicular directions for each pixel, , . This is performed by twice using a 1D convolution with the kernel approximating the derivative.
3. For each pixel and a given neighborhood window:
  Calculate the local structure matrix .
  Evaluate the response function .
4. Choose the best candidates for corners by selecting a threshold on the response function and perform non-maximal suppression.

## Slide 33: Detection of maximally stable extremal regions
If the image is rescaled or transformed projectively, the output of a Harris detector changes rapidly.
Maximally Stable Extremal Regions (MSERs) are an example of an image structure that can be repeatably detected not only after translations and rotations, but also after similarity and affine transforms.
  Informally, MSERs can be explained by imagining all possible thresholdings of an input gray-level image .
  We will refer to the pixels below a threshold as ‘black’ and to those above or equal as ‘white’.
  If we shown a movie of thresholded image with frame corresponding to threshold we will see first a white image, and the last image is black.
  The connected components in these frames are the set of maximal regions.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 34: Maximally Stable Extremal Regions
http://vision.princeton.edu/projects/2012/SUN360/CVPR2012code/code/vlfeat-0.9.5/doc/api/mser_8h.html

## Slide 35: Maximally Stable Extremal Regions
https://www.youtube.com/watch?v=b2pLUxB9Vaw

## Slide 36: Detection of maximally stable extremal regions
Maximally Stable Extremal Regions (MSERs) have the following properties.
  Invariance to monotonic transformations.
  If
  where is a transformation.
  Invariance to adjacency preserving (continuous) transformations.
  Stability, since only extremal regions whose support is virtually unchanged over a range of thresholds are selected.
  Multi-scale detection. Since no smoothing is involved, both very fine and very large structure is detected.
  The set of all extremal regions can be enumerated in , almost in linear time for 8 bit images.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 37: Enumeration of extremal regions
Algorithm 5.6 Enumeration of extremal regions
1. Sort image pixels by intensity; this can be done efficiently by, e.g., binsort, in time.
2. Starting at the minimum intensity , iterate upward.
3. Consider pixels of the current intensity ; introduce the pixel and update the connected component structure. This may be done using the efficient union-find algorithm [Sedgewick,1998].
4. If two regions marge, this is viewed as the death of the smaller component.
5. When all intensities have been processed, we have a data structure holding the area of each connected component as a function of a threshold.
If are a sequence of nested extremal regions, so , then extremal region is maximally stable iff has a local minimum at , where denotes cardinality and is a parameter of the method.

## Slide 38: Detection of maximally stable extremal regions
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 39: Image restoration
Pre-processing methods that aim to suppress degradation using knowledge about its nature are called image restoration. (影像還原;影像復原)
Most image restoration methods are based on convolution applied globally to the whole image.
Image restoration techniques can be classified as deterministic or stochastic.
  Deterministic (決定論的) methods are applicable to images with little noise and a known degradation function.
  Stochastic (隨機的) techniques try to find the best restoration according to a particular statistical criterion, e.g., a least-square method.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 40: Image restoration
Three typical degradations with a simple function
  Relative constant speed movement of the object with respect to the camera
  Wrong lens focus
  Atmospheric turbulence (大氣亂流)
In most practical cases, there is insufficient knowledge about the degradation, and it must be estimated and modeled.
  A priori knowledge: known in advance or obtained before restoration
    For example, the parameters of a device (camera)
  A posteriori knowledge: obtained by analyzing the degraded image
    For example, the interest points in the image
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 41: An example—Object moving
http://www.robots.ox.ac.uk/~az/lectures/ia/lect3.pdf

## Slide 42: An example—Wrong lens focus
http://www.robots.ox.ac.uk/~az/lectures/ia/lect3.pdf

## Slide 43: An example—Atmospheric turbulence
https://www.udayton.edu/engineering/research/signal-and-image-processing-lab/research/index.php

## Slide 44: Image restoration
A degraded image can arise from the original image by
where is some non-linear function and describes the noise.
It can be simplified by neglecting the non-linearity and assuming that the function is invariant with respect to position in the image.
If the noise is not significant in this equation, the restoration equates to inverse convolution.
If noise is not negligible, then the inverse convolution is solved as an overdetermined system of linear equations.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 45: Image restoration
Degradations that are easy to restore
  Since , in the Fourier domain,
Case 1: Relative motion of camera and object
  Suppose is the constant speed in the direction of the axis, be the shutter open time. The Fourier transform of the degradation caused in time is give by [Rosenfeld and Kak, 1982]
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 46: Image restoration
Case 2: Wrong lens focus
  Image smoothing caused by imperfect focus of a thin lens can be described by the function [Born and Wolf, 1969]
where is the Bessel function of the first order, , and is the displacement.
The model is not space invariant.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
由Alessio Damato - own work本向量圖形使用gnuplot創作。https://commons.wikimedia.org/w/index.php?curid=365944

## Slide 47: Image restoration
Case 3: Atmospheric turbulence
  Atmospheric turbulence is degradation that needs to be restored in remote sensing (遙測) and astronomy (天文學).
  One mathematical model [Hufnagel and Stanley, 1964] is
  where is a constant that depends on the type of turbulence which is usually found experimentally.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 48: Image restoration
Inverse filtering
  Inverse filtering assumes that
    degradation was caused by a linear function
    consider the additive noise as another source of degradation
    additive noise is independent of the signal
  After applying the Fourier transform
  The original image (its Fourier transform to be exact)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 49: Image restoration
Wiener (least mean square) filtering
  Wiener filtering attempts to take account of noise properties by incorporating a priori knowledge in the image restoration formula.
  Restoration by the Wiener filter gives an estimate of the original image with minimal mean square error.
where denotes the mean operator.
  Denote the Fourier transform of the Wiener filter by .
  The estimate of the Fourier transform of the original image can be obtained as
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 50: Image restoration
Wiener (least mean square) filtering
  The estimate of the Fourier transform of the original image can be obtained as
  is not derived here, but may be found elsewhere [Gonzalez and Woods, 1992] as
  where : the transform function of the degradation.
  : the complex conjugate
  : the spectral density of the noise
  : the spectral density of the undegraded image
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
http://homepages.inf.ed.ac.uk/rbf/CVonline/LOCAL_COPIES/VELDHUIZEN/node15.html
https://en.wikipedia.org/wiki/Spectral_density

## Slide 51: Image restoration
An restoration example of an image that was degraded by 5 pixels motion in the direction of the axis
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle